## Slide 1: Introduction and Camera Overview Martin Nordby Chief Mechanical Engineer LSST Camera Safety Review August 18, 2015
R1

## Slide 2: Camera Safety Review Agenda
Introduction (25 minutes, Nordby)
LSSTCam PSAP and safety overview (20 minutes, Kenny)
  System safety, SLAC ES&H during I&T, review process, subject-matter safety
Hazard analysis process (20 minutes, Kenny)
  HAR and SSPP process details and outcome
  Hazard List—details of camera hazards and mitigation (identify operating hazards)
Camera protection system (15 minutes, Nordby)
  General plans for protection system functionality
Camera design and hazard mitigations (60 minutes, O’Neill)
  Walk through subsystems and hazard mitigations/controls built into the design
I&T hazards (30 minutes, Nordby/Bond)
  Plans for capturing and addressing hazards; training-auth-release of work
  WP&C; seismic; high-value lifts and handling; brittle materials
  I&T process flow
  Maintenance planning
Camera hazards on the summit (30 minutes, Kenny)
  Clean rooms; on-telescope
  Further work: LOTO, access control, ODH and clean- and utility- room monitoring, hazards associated with maintenance, hoisting and rigging, fall protection, confined space

## Slide 3: Camera Safety Review Agenda
Introduction (25 minutes, Nordby)
LSSTCam PSAP and safety overview (20 minutes, Kenny)
Hazard analysis process (20 minutes, Kenny)
Camera protection system (15 minutes, Nordby)
Camera design and hazard mitigations (60 minutes, O’Neill)
I&T and Operating and Support Hazards (30 minutes, Nordby/Bond)
Camera hazards on the summit (30 minutes, Kenny)

## Slide 4: Charge
Has the Camera System Safety Program established the appropriate systems and processes to ensure the delivery of the Camera in a safe and environmentally sound manner?
Is safety adequately integrated into the camera system and subsystems?
Is the LSST Camera team effectively
  Identifying hazards
  Characterizing the hazards
  Assessing the associated risk
  Establishing appropriate controls to reduce the risk to acceptable levels
  Identifying means to verify that the controls are implemented

## Slide 5: Camera Final Design Overview

## Slide 6: Camera assembly
Scale
1000 mm
Light baffles
Carousel holding off-line Filters
Cryostat
Shutter
Auto Changer
L1 lens
L2 lens
Filter
Detector plane
Shroud
Camera Body
L3 lens
Utility Trunk
Auxiliary electronics
Refrigeration system heat exchangers
Camera Parameters | 
Depth-of-focus | f 1.2
Focal plane diameter | 634 mm
Maximum mass | 3000 kg
Maximum diameter | 1650 mm
Total length | 3732 mm

## Slide 7: Camera focal plane with 201 sensors
Guide Sensors
(8 locations)
Wavefront Sensors
(2 half-WFS at 4 locations)
3.5 degree Field of View (634 mm diameter)
Wavefront - Curvature Sensor Side View Configuration
Focal plane
4 mm
40 mm
Sci CCD
Science Sensors (189 locations)
Science Raft Sensor Assembly (RSA)
(21 locations)
Corner Raft Sensor Assembly (RSA)
(4 locations)

## Slide 8: Science and guide sensors
e2V sensor
ITL sensor
Prototype sensors
Profile measurement of a sensor
CCD Sensors
3.2 Gigapixels
10 micron (0.2 arcsec) pixels
2 second read-out
Spectral coverage: 350–1040nm
Silicon CCD bonded to ceramic circuit board and ceramic/invar structure
Vulnerabilities
Thin, brittle sensors
ESD-sensitive circuits
Sensor performance affected by contamination
5 voltages require sequenced power-up

## Slide 9: Sensors mounted to raft sensor assemblies
Science Raft Sensor Assembly
Corner Raft Sensor Assembly
Science sensor
Guide sensor
Prototype sensors on a raft plate
Raft Baseplate
Thermal Strap
Wavefront sensor
Raft Sensor Assembly
Silicon-carbide baseplate to maximize stiffness and thermal behavior
Sensors registered to baseplate with precision posts and screwed in place
Nominal gap between sensors: .25 mm
Heaters on baseplate stabilize CCD temperatures
Vulnerabilities
Brittle SiC baseplate material
Tapped holes in SiC may produce dust
Small gaps between sensors
V-groove mounts see high contact stresses

## Slide 10: Raft sensor assemblies and raft tower modules
Science Raft Tower Module
Corner Raft Tower Module
Raft Electronics Board (REB)
Prototype RTM structure and Base Plate
Raft Tower Module
1 REB provides voltages, read-out control, and image digitizing for 3 CCDs
Stack of 3 REBs mount to REC
RSA is held to Grid with spring-loaded hold-downs
Gap between CCDs on neighboring rafts: .5 mm
Vulnerabilities
REB components can outgas in vacuum
RTMs integrate with very small clearances
Long thermal path with contact resistances

## Slide 11: Cryostat assembly with raft towers integrated
Grid support structure (-130 C)
Cryostat Housing
Instrumentation flange
Vacuum-insulated refrigerant lines (-135 C)
Cryo Plate (-135 C)
Grid K-C ball test
Cryo Plate braze test
Cold Plate (-40 C)
Sensors (-100 C)
Cryostat Integrating Structure
SiC Grid provides stable support for CCD detectors on focal plane
Cryo plate provides thermal control of cold CCDs
Cold plate removes REB process heat
Provides pumping and monitoring for clean high-vacuum environment
Vulnerabilities
Refrigerant leak in cryostat would contaminate CCDs and clean components
SiC Grid structure is brittle
Vacuum sealing and pumping is vital to reduce risk of contamination

## Slide 12: Cryostat with L3 lens and vacuum pumping hardware
L3 Lens Assembly
Vacuum system components
L3 Lens stress analysis
Cryostat support cylinder
L3 Lens Assembly
Entrance window into cryostat
Holds off atmospheric pressure load
Includes double vacuum seal
Titanium flange allows for thermal and structural isolation of lens from cryostat
Vulnerabilities
Brittle material under stress
Lens/flange/cryostat CTE mismatches

## Slide 13: Cryostat and refrigeration system heat exchangers
Heat exchanger units
Vacuum-insulated transfer lines
Heat exchanger prototype
Fully articulating sub-scale prototype
Refrigeration Systems
Cryo system removes 540 W at -130 C from CCD heating, L3 radiation, conduction
Cold system removes 1500 W at -40 C from REB boards
8 parallel systems use commercial hermetically sealed compressors units
Compressors on telescope keel beam

## Slide 14: Cryostat and fully loaded utility trunk
Utility trunk
Cryostat
Vacuum components
Auxiliary electronics
L3 Lens Assembly
Region accessible while mounted to telescope
Utility Trunk Integrating Structure
Houses utilities and electronics
Provides a single location for disconnect of all lines to the Camera
Cools all support utilities using glycol
Allows for access to electronics crates during camera servicing
Maintains clean, sealed environment

## Slide 15: Carousel assembly holding 5 on-board filters
Carousel structure
Back Flange
Filters
Carousel X- filter clamp test unit
Filter demonstration unit
Filter clamp
Vulnerabilities
Control of carousel clamp and rotation mechanisms
Kinematic supports result in many single failure point items
Stresses in thin filters
Carousel
Stores 5 filters in the clean environment of the Camera
Moves filter into the hand-off position for bringing on-line
Clears cryostat
Filters
6 filters provide broad spectral range
Spherical radii and variable thickness of filters handled by standard frame design
Frame held kinematically

## Slide 16: Camera body and back flange
Camera housing
Camera
back flange
Access ports
Camera Body Integrating Structure
Provides primary support for L1-L2 Ass’y, Auto Changer, Shutter
Maintains clean, hermetically sealed environment for all optics
Presents primary structural interface to telescope at back flange
Presents primary thermal interface to telescope at outer housing
Vulnerabilities
High local loads and mount points
Must sustain 5.7 g seismic loads
Carries ~5 kPa internal pressure

## Slide 17: Shutter mounts to front flange of the camera body
Shutter
Vulnerabilities
High blade speeds (~1.5 m/sec)
Close clearances to optics
Two blade stacks run on one rail
Shutter
1 sec open/close time
734 mm opening aperture
1E6 cycles per year
Fits between filter and L3

## Slide 18: Auto changer moves filters from the Carousel into the on-line position
Auto Changer
Filter
Filter Loader prototype
On-Line Clamp test unit
Filter Loader mount port
Exchange System
Supports a filter in the on-line position
Moves filter into the field of view by remote command
Change time < 90 sec
Filter diameter ~800 mm
Accommodates swap out of filter from camera
Vulnerabilities
Control of clamp and drive mechanisms
Kinematic supports result in single failure points
Drive train component failure or loss of function

## Slide 19: Exchange system motion and single-filter prototype test videos
Exchange system motions
Single filter test unit in Marseille, FR

## Slide 20: Fully loaded cryostat integrated into Camera assembly
Detector plane through Filter and L3
Utility Trunk

## Slide 21: L1-L2 assembly mounted to the Camera front flange
L1-L2 assembly
L1-L2 mounting struts
Camera shroud support frame
L1-L2 Assembly
L1 lens is 1.6 m diameter
L1 and L2 lens aligned and tested as a unit
L1-L2 assembly supported kinematically
Struts allow for aligning the assembly
CFC structure provides rigidity
Vulnerabilities
Large, heavy lenses
Single failure point struts
Bonded joints and flexures under high stress
Bonded CFC structure

## Slide 22: Camera with shroud—fully assembled
Camera Body
Utility Trunk
L1-L2 assembly
Camera Shroud

## Slide 23: Camera assembly

## Slide 24: Camera design summary
Nearly all subsystems of the camera have been subjected to a Final Design Review, including review of subsystem hazards and controls
  Remaining FDRs: refrigeration system, camera body, shutter, utility trunk, auxiliary electronics
Subsystem hazards have been identified and their definitions refined as subsystem designs have matured over the years
  Hazard design mitigations are included in the final design
  Hazard controls have been incorporated into the control and protection systems
  Administrative controls have been flagged as operating and support hazards and are scheduled to be further addressed at subsystem Manufacturing Readiness Reviews